## Slide 1
5 Transmission media
2 types of transmission media:
Physical Transmission
Wireless Transmission

## Slide 2: Physical Transmission Twisted Pair cable, UTP
Unshielded twisted pair cable (UTP)
Types: CAT 3, CAT 5, 5E, 6, 7
Maximum cable length: 100m
Metal core, electrical signals
Only one network signal can travel along a cable at a time
Poorly shielded from electromagnetic interference
Bandwidth: 10, 100, 1 GB, (5E), 10 GBS, (7)
Used in star networks

## Slide 3: Physical Transmission Twisted Pair cable, Coaxial Cable
Contains only two wires
Carry data 185 mtrs at 10 Mbps
Used in bus networks where all data travels in both directions away from any computer that originates a message
Rarely used now except for cable internet

## Slide 4: Physical Transmission: Fibre Optic Cable, FOC
Glass or plastic core that transmits Optical (laser light) signals
Max length: kilometres (no electrical resistance = little signal fade)
Immune to EMI (electromagnetic interference)
MASSIVE bandwidth & speed; (The amount of data that can be transmitted in a fixed amount
of time).
Expensive connectors needed at each end to convert between optical/electrical network signals
FOC for long distances (>100m), across
oceans, between distant sites

## Slide 5: Physical Transmission: Fibre Optic Cable, FOC
Fibre optics advantages:
Fibre optic cables have a much greater bandwidth than metal cables. This means that they can carry more data.
Fibre optic cables are less susceptible than metal cables to interference.
Fibre optic cables are much thinner and lighter than metal wires. Data can be transmitted digitally
Disadvantage of fibre optics is that the cables are expensive to install. In addition, they are more fragile than wire and are difficult to splice.

## Slide 6: Wireless Transmission
Radio Waves
For radio transmissions to occur a transmitter and a receiver is required
Wi-Fi networks use radio waves
More flexible than cable but slower
Bluetooth uses short-range radio waves to transmit data, up to 10 mtrs. Data transfer of 2Mbps c/f Wi-Fi of up t0 108 Mbps

## Slide 7: Wireless Transmission
Microwaves
Require line-of-sight transmission
Very high data rates, eg. 4 Mbps over 5 kms.
Satellite
In the form of radio waves or microwaves
Average download rate 1 Mbps
Limitations: distance the waves have to travel to the satellite & back & among the most expensive ways of gaining broadband Internet access
in rural areas it may be the only choice

## Slide 8: Wireless Transmission
Microwaves
Require line-of-sight transmission
Very high data rates, eg. 4 Mbps over 5 kms.
infra-red transmission
Uses light waves & requires line-of sight
Effective up to 5 mtrs
Slow data transfer rates but can be useful with hand held computers with this port to communicate to printers or pc